## Slide 1: Computational Thinking & Systems Design Lecture 02: from Logic to Arithmetic
Ben Koo
September 22, 2020

## Slide 2
Week 1 Review: Test Driven Design on Chips
Summary:
Test Driven Design: Logical correctness is verified through “Test Cases”.
There are many equivalent languages or models of computation(MoC) :
  Truth Table、Logic Circuit、Hardware Description Language (HDL), …
  Correspondence between MoC：Curry-Howard-Lambek Isomorphism
Complexity comes from composing simple things
  There are total of 6 different 2 inputs/1 output logic gates (NAND/NOR …) that are considered to be “Universal Components”
  You should be watching Nand2Tetris and Computational Structure’s first week video
  Learn the whole stack by building a Blockchain-recorded Go game

## Slide 3
Week 1 References:
Videos:
Coursera Video website: https://www.coursera.org/learn/build-a-computer
Computer Science by PBS: https://youtu.be/gI-qXk7XojA
  Boolean Logic & Logic Gates: Crash Course Computer Science #3

## Slide 4
  Languages ~= Models of Computation
The era of Super-Human Intelligence
  The classification of intelligence is determined by the use of Languages
  Formal Languages has computable objects: Vocabulary, Grammar, Semantics
From Logics to Number Systems: The Workhorse of Turing Complete Computation: Arithmetic Logic Unit
Memory: The Space-Time Entanglement of Digital Circuitry
Composition: The idea behind the assembly language
  From Binary Notation to Human Mnemonics

## Slide 5: Tools and Books are freely available for building complex systems
http://chimera.labs.oreilly.com/books/1234000000754/index.html

## Slide 6
Overview of the Nand2Tetris System
Virtual Machine
Layer 5
Software
hierarchy
Assembly Language
Layer 4
Hardware
hierarchy
Machine Language
Layer 3
Hardware Platform
Layer 2
Chips and Logic Gates
Layer 1
Human
Thought
Physics
Chapter 10-11
Compiler
Chapter 9-12
VM Translator
Chapter 7-8
High Level Language
Layer 7
Operating System
Human Machine Interfaces
User Defined Applications
Layer 6
Chapter 6
Chapter 4-5
Computer Architecture
Electrical Engineering
Chapter 1-3
Logics and Arithmetic
Knowledge Representation
Systems Design
Chapter 13-15
Product/Service Design

## Slide 7
Class Screen {
function void clearScreen()
function void setColor(boolean b)
function void drawPixel(int x, int y)
function void drawLine(int x1, int y1, int x2, int y2)
function void drawRectangle(int x1, int y1, int x2, int y2)
function void drawCircle(int x, int y, int r)
}
Operating System Maps to the other Layers
Virtual Machine
Layer 5
Assembly Language
Layer 4
Machine Language
Layer 3
Hardware Platform
Layer 2
Chips and Logic Gates
Layer 1
High Level Language
Layer 7
Operating System
Human Machine Interfaces
User Defined Applications
Layer 6
class Math {
function void init()
function int abs(int x)
function int multiply(int x, int y)
function int divide(int x, int y)
function int min(int x, int y)
function int max(int x, int y)
function int sqrt(int x)
}
Class Keyboard {
function char keyPressed()
function char readChar()
function String readLine(String message)
function int readInt(String message)
}
class Memory {
function int peek(int address)
function void poke(int address, int value)
function Array alloc(int size)
function void deAlloc(Array o)
}
Class Sys {
function void halt():
function void error(int errorCode)
function void wait(int duration)
}
class Output {
function void moveCursor(int i, int j)
function void printChar(char c)
function void printString(String s)
function void printInt(int i)
function void println()
function void backSpace()
}
Class Array {
function Array new(int size)
method void dispose()
}
Class String {
constructor String new(int maxLength)
method void dispose()
method int length()
method char charAt(int j)
method void setCharAt(int j, char c)
method String appendChar(char c)
method void eraseLastChar()
method int intValue()
method void setInt(int j)
function char backSpace()
function char doubleQuote()
function char newLine()
}

## Slide 8
Class Screen {
function void clearScreen()
function void setColor(boolean b)
function void drawPixel(int x, int y)
function void drawLine(int x1, int y1, int x2, int y2)
function void drawRectangle(int x1, int y1, int x2, int y2)
function void drawCircle(int x, int y, int r)
}
A Strategy to Finish all 12 Stages of systems
Virtual Machine
Layer 5
Assembly Language
Layer 4
Machine Language
Layer 3
Hardware Platform
Layer 2
Chips and Logic Gates
Layer 1
High Level Language
Layer 7
Operating System
Human Machine Interfaces
User Defined Applications
Layer 6
class Math {
function void init()
function int abs(int x)
function int multiply(int x, int y)
function int divide(int x, int y)
function int min(int x, int y)
function int max(int x, int y)
function int sqrt(int x)
}
Class Keyboard {
function char keyPressed()
function char readChar()
function String readLine(String message)
function int readInt(String message)
}
class Memory {
function int peek(int address)
function void poke(int address, int value)
function Array alloc(int size)
function void deAlloc(Array o)
}
Class Sys {
function void halt():
function void error(int errorCode)
function void wait(int duration)
}
class Output {
function void moveCursor(int i, int j)
function void printChar(char c)
function void printString(String s)
function void printInt(int i)
function void println()
function void backSpace()
}
Class Array {
function Array new(int size)
method void dispose()
}
Class String {
constructor String new(int maxLength)
method void dispose()
method int length()
method char charAt(int j)
method void setCharAt(int j, char c)
method String appendChar(char c)
method void eraseLastChar()
method int intValue()
method void setInt(int j)
function char backSpace()
function char doubleQuote()
function char newLine()
}
Start with the Operating System as you go.

## Slide 9
Given: Nand(a,b), false
We can build:
Not(a) = Nand(a,a)
true = Not(false)
And(a,b) = Not(Nand(a,b))
Or(a,b) = Not(And(Not(a),Not(b)))
Xor(a,b) = Or(And(a,Not(b)),And(Not(a),b)))
Etc.
George Boole, 1815-1864
(“A Calculus of Logic”)
  Boolean algebra

## Slide 10
Xor(a,b) = Or(And(a,Not(b)),And(Not(a),b)))
Implementation
Interface
Claude Shannon, 1916-2001
(“Symbolic Analysis of Relay and Switching Circuits” )
  Gate logic

## Slide 11
Gate logic – a gate architecture designed to implement a Boolean function
Elementary gates:
Composite gates:
Important distinction: Interface (what) VS implementation (how).
  Gate logic

## Slide 12
Proposed Implementation: based on Not, And, Or gates.
a b sel out
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 0
1 1 0 1
1 1 1
sel out
0 a
1 b
  Multiplexer

## Slide 13
a b out
0 0 0
0 1 0
1 0 0
1 1 1
And.cmp
load And.hdl,
output-file And.out,
compare-to And.cmp,
output-list a b out;
set a 0,set b 0,eval,output;
set a 0,set b 1,eval,output;
set a 1,set b 0,eval,output;
set a 1, set b 1, eval, output;
And.tst
And.hdl
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
Contract:
When running your .hdl on our .tst, your .out should be the same as our .cmp.
  Example: Building an And gate

## Slide 14
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
And.hdl
Interface: And(a,b) = 1 exactly when a=b=1
  Building an And gate

## Slide 15
Implementation: And(a,b) = Not(Nand(a,b))
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
And.hdl
  Building an And gate

## Slide 16
Implementation: And(a,b) = Not(Nand(a,b))
CHIP And
{ IN a, b;
OUT out;
// implementation missing
}
And.hdl
  Building an And gate

## Slide 17
CHIP And
{ IN a, b;
OUT out;
Nand(a = a, b = b, out = x);
Not(in = x, out = out)
}
Implementation: And(a,b) = Not(Nand(a,b))
And.hdl
  Building an And gate

## Slide 18
test script
HDL program
  Hardware simulator (demonstrating Xor gate construction)

## Slide 19
  PBS Series: Crash Course on Computer Science
https://youtu.be/1I5ZMmrOfnA

## Slide 20
  Main Ideas on Week 2 Project
Hack Computer uses a 16 bit Architecture (1 bit for Sign)
  Number ranges from (- 32768 to 32768)
Subtraction is accomplished through adding “complement value”
A Full Adder is composed of two Half Adders (Carry bit)
ALU is purely combinatorial, no memory

## Slide 21: Counting systems
quantity decimal binary 3-bit register
0 0 000
 1 1 001
 2 10 010
 3 11 011
 4 100 100
 5 101 101
 6 110 110
 7 111 111
 8 1000 overflow
 9 1001 overflow
 10 1010 overflow

## Slide 22: Rationale

## Slide 23
no overflow
overflow
Algorithm: exactly the same as in decimal addition
Overflow (MSB carry) has to be dealt with.
Binary addition
Assuming a 4-bit system:
0 0 0 1
1 0 0 1
0 1 0 1
0 1 1 1 0
+
1 1 1 1
1 0 1 1
0 1 1 1
1 0 0 1 0
+

## Slide 24: Representing negative numbers (4-bit system)
The codes of all positive numbers begin with a “0”
The codes of all negative numbers begin with a “1“
To convert a number: leave all trailing 0’s and first 1 intact, and flip all the remaining bits
0 0000
1 0001 1111 -1
2 0010 1110 -2
3 0011 1101 -3
4 0100 1100 -4
5 0101 1011 -5
6 0110 1010 -6
7 0111 1001 -7
1000 -8
Example: 2 - 5 = 2 + (-5) = 0 0 1 0
+ 1 0 1 1
1 1 0 1 = -3

## Slide 25: Building an Adder chip
Adder: a chip designed to add two integers
Proposed implementation:
  Half adder: designed to add 2 bits
  Full adder: designed to add 3 bits
  Adder: designed to add two n-bit numbers.

## Slide 26: Half adder (designed to add 2 bits)
Implementation: based on two gates that you’ve seen before.
a b sum carry
0 0 0 0
0 1 1 0
1 0 1 0
1 1 0 1

## Slide 27: Full adder (designed to add 3 bits)
Implementation: can be based on half-adder gates.
a b c sum carry
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1

## Slide 28: n-bit Adder (designed to add two 16-bit numbers)
Implementation: array of full-adder gates.
... 1 0 1 1 a
… 0 0 1 0 b
… 1 1 0 1 out
+

## Slide 29: The ALU (of the Hack platform)
out(x, y, control bits) =
x+y, x-y, y–x,
0, 1, -1,
x, y, -x, -y,
x!, y!,
x+1, y+1, x-1, y-1,
x&y, x|y

## Slide 30: ALU logic (Hack platform)
Implementation: build a logic gate architecture that “executes” the control bit “instructions”: if zx==1 then set x to 0 (bit-wise), etc.

## Slide 31
The ALU in the CPU context (a sneak preview of the Hack platform)
ALU
Mux
D
out
A/M
a
D register
A register
A
M
c1,c2, … ,c6
RAM
(selected register)

## Slide 32: Perspective
Combinational logic
Our adder design is very basic: no parallelism
It pays to optimize adders
Our ALU is also very basic: no multiplication, no division
Where is the seat of more advanced math operations? a typical hardware/software tradeoff.

## Slide 33
  CPU is “Universal” (万用)
http://www.visual6502.org/JSSim/index.html
https://en.wikipedia.org/wiki/MOS_Technology_6502

## Slide 34: Historical end-note: Leibnitz (1646-1716)
“The binary system may be used in place of the decimal system; express all numbers by unity and by nothing”
1679: built a mechanical calculator (+, -, *, /)
CHALLENGE: “All who are occupied with the reading or writing of scientific literature have assuredly very often felt the want of a common scientific language, and regretted the great loss of time and trouble caused by the multiplicity of languages employed in scientific literature:
SOLUTION: “Characteristica Universalis”: a universal, formal, and decidable language of reasoning
The dream’s end: Turing and Gödel in 1930’s.
Leibniz’s medallion for the Duke of Brunswick

## Slide 35: Gödel Numbering
In mathematical logic, a Gödel numbering is a function that assigns to each symbol and well-formed formula of some formal language a unique natural number, called its Gödel number. The concept was used by Kurt Gödel for the proof of his incompleteness theorems. (Gödel 1931)
  https://en.wikipedia.org/wiki/G%C3%B6del_numbering#CITEREFG.C3.B6del1931
Kurt Gödel’s picture from Wikipedia

## Slide 36: Cellular Automata
A cellular automaton (pl. cellular automata, abbrev. CA) is a discrete model studied in computability theory, mathematics, physics, complexity science, theoretical biology and microstructure modeling. Cellular automata are also called cellular spaces, tessellation automata, homogeneous structures, cellular structures, tessellation structures, and iterative arrays.
  https://en.wikipedia.org/wiki/Cellular_automaton
John Horton Conway
Picture from Wikipedia
Cellular Automaton picture from Wikipedia

## Slide 37
Application level: Go (by: José Luis Gómez-Muñoz)

## Slide 38
Your ability in identifying proper reference material
  Learn from the Internet and Public Libraries
  Use relevant data sources and provide argument for its validity
Your interpretation of content
  Reflected in your documentation and implementation of the Go System
Grade Distribution
  20% 课上参与， 40% 软件作业， 20% 学习报告，20% 教科书。
  Grading Policy