## Slide 1: Computational Thinking & Systems Design The Whole Computer
Ben Koo
October 13, 2020
Summa de arithmetica, geometria, proportioni et proportionalita (Summary of arithmetic, geometry, proportions and proportionality) is a book on mathematics written by Luca Pacioli and first published in 1494. It contains a comprehensive summary of Renaissance mathematics, including practical arithmetic, basic algebra, basic geometry and accounting, written for use as a textbook and reference work.
Wikipedia link

## Slide 2: Prelude
Architecture: stable properties of a system
  Architectural properties govern system performance
  Architectural classification guides system design decisions
  The essence of computing architecture is in:
    arithmetic operations, storage, and communication
    It relation to CAP theorem:
      Consistency, Availability, Partition Tolerance

## Slide 3: Architectural Analysis has its roots in Math
How computation could work is grounded in arthmetics, geometry, and proportionality…
Youtube video link

## Slide 4: The Hierarchy of Complexity
Image Source: https://en.wikipedia.org/wiki/Turing_machine

## Slide 5: An example of Automaton
Image Source: https://en.wikipedia.org/wiki/Turing_machine
The state bounds of
busy beaver
(according to Wikipedia)

## Slide 6: The Notion of Universal Component/Instruction
ENIAC inventors John Mauchly and J. Presper Eckert proposed the EDVAC's construction in August 1944.
Creating a complete set of
Arithmetic instruction is the foundation of computing.

## Slide 7: Arithmetic Operations on Paper
A way to perform multiplication using matrix layout in Pacioli’s book.

## Slide 8: Hybrid Architecture Example
Neural Network
Image Processing
Machine Learning
Von Neumann Architecture
Graphics Processing
Dedicated Security

## Slide 9: Computer Architectures
Quantum Computing
Architecture
Human Computing
Architecture
Please refer to Captcha
https://www.wikiwand.com/en/CAPTCHA
Please refer to Agent-based Computing
i.e. NetLogo
Notes: 9

## Slide 10: Computing and Spacetime
如果我不运行计算机，或者说让计算机待机，那么电脑就会处于一种类似于休息的状态。其实这么说也没错，但实际上还是有点不一样的。计算机实际上每时每刻都在执行命令，ALU从不停止。ALU每个时钟周期都在干活，输出结果，状态位，PC一直在产一条指令的地址。我们所认为的计算机待机，其实只是电脑在空循环。这个说法也有对的地方。因为空循环的能耗确实小于使用中。空循环时除了最基本的CPU供电以外，需要隔一定时间去刷新主存防止因漏电导致数据丢失。
Oct 2020 郑吉源
Notes: 10

## Slide 11: Quantum Terminology
Superposition compresses time
Entanglement collapses space
Notes: 11

## Slide 12: CISC versus RISC Instruction Sets
Notes: 12

## Slide 13: ARM versus Intel Instruction Sets
Notes: 13

## Slide 14
History of CPU Development

## Slide 15: Industrial and World Dynamics
The World is made of three kinds of things:
Stock, Flow, and State variables parameterized in time

## Slide 16
The Vax 11/780 Computer

## Slide 17: What is Hyper-threading?

## Slide 18: What is a Mother Board?

## Slide 19: Quantum Computing Architecture
Stack Exchange: How a Quantum Computer can be programmed?

## Slide 20
Google CEO on Automated Machine Learning
Automated Learning to Learn is here!

## Slide 21: Soundness
Every provable statement is true
Completeness
Every true statement is provable
Cited from : Soundness and Completeness: With Precision on news.ycombinator.com
Can we come up with a sound and complete computing architecture classification scheme?

## Slide 22
The Master Algorithm that will rule the world?
22
The thesis:
Processing data through a single universal learning algorithm— can get all the knowledge from the past, the present, and the future
Pedro Domingos, TMA, P. 25
Bill Gates recommended this book
in 2016 Code Conference
Chinese Translation
President Xi’s
Bookshelf

## Slide 23
The Five Flavors of Master Algorithm
Image Source: Master Algorithm

## Slide 24
Scientific Revolution
Neutral Network
Symbolic Logic
Causal Probability
Cognitive Semantics
IoT and Quantum Computing
TPU
GPU
CPU
Big Data
Computed Data
Artificial Data
Distributed
Centralized
General Protocol
Software
Hardware
Content
Standard
Thinking
T. Kuhn
Collective learning systems
Computing Architectures, Instrumentation
Data Assets, Structures
J. Hinton
N. Chomsky
S. Wolfram
J. Pearl
Governance Strategies
Encoding strategy, Ontology, Epistemology
Extreme Learning Process
An integrated (ethical) architecture
to implement the Master Algorithm

## Slide 25
The 3 Generalized Computing Tasks
and how AI relates to them
Capability | AI inspired threats | Solution to AI threats
Search | Digesting overwhelming amount of knowledge | Apply search to private knowledge
Optimize | Solve problems assumed to be impossible | Become aware when impossible become possible
Simulate | Offer future plans at rates much higher than traditional wisdom | Update inadequate possibility model of our surroundings

## Slide 26: Approximate Truth through Multiple Abstractions
Look into Abstract Interpretation by Patrick and Radhia Cousot
  The invention of Widening and Narrowing Operators
  Known in the area known as Static Analysis

## Slide 27
The Rosetta Stone by John Baez
Image source: wikipedia

## Slide 28
The Rosetta Stone of Scientific Languages
Biology | Math | Physics | Cybernetics/System Sciences
Homeostasis/DNA | Iterative/Recursive Functions | Multi-Scale Interactions | Feedback Loops
Cellular Construction/Boundary Setting | Difference/Differentiation | Observations | Data Collection
Lifespan Expansion | Integration | Spacetime Accumulation | Statistical Interpretation
Entropy Negation | Numbers/Generative Name Spaces/Algebras | “Unified” Theory | From Theory to Applications and Back

## Slide 29
A mathematical Language for
Real Applications that are computationally intensive

## Slide 30: Classifying Architecture based on Spacetime properties
Cloud Computing
Abstract Specification
Deterministic
Probabilistic
Centralized
Hybrid
Distributed
Single/Multi Core
Many Core
Single Site
Multi Site
Many Site
Notes: 30

## Slide 31: Processing logic: fetch-execute cycle
Executing the current instruction involves one or more of the following micro-tasks:
  Have the ALU compute some function out = f (register values)
  Write the ALU output to selected registers
  As a side-effect of this computation, figure out which instruction to fetch and execute next.

## Slide 32: The Hack computer
Main parts of the Hack computer:
Instruction memory (ROM)
Memory (RAM):
  Data memory
  Screen (memory map)
  Keyboard (memory map)
CPU
Computer (the logic that holds everything together).
A 16-bit Von Neumann platform
The instruction memory and the data memory are physically separate
Screen: 512 rows by 256 columns, black and white
Keyboard: standard
Designed to execute programs written in the Hack machine language
Can be easily built from the chip-set that we built so far in the course

## Slide 33: Main Parts of the Hack Computer
Instruction memory (ROM)
Memory (RAM):
Data memory
Screen (memory map)
Keyboard (memory map)
CPU
Computer (the logic that holds everything together).

## Slide 34: Data memory
Low-level (hardware) read/write logic:
To read RAM[k]: set address to k, probe out
To write RAM[k]=x: set address to k, set in to x, set load to 1, run the clock
High-level (OS) read/write logic:
To read RAM[k]: use the OS command out = peek(k)
To write RAM[k]=x: use the OS command poke(k,x)
peek and poke are OS commands whose implementation should effect the same behavior as the low-level commands
More about peek and poke this later in the course, when we’ll write the OS.
load

## Slide 35: Screen
The Screen chip has a basic RAM chip functionality:
  read logic: out = Screen[address]
  write logic: if load then Screen[address] = in
Side effect:
Continuously refreshes a 256 by 512 black-and-white screen device
The bit contents of the Screen chip is called the “screen memory map”
The simulated 256 by 512 B&W screen
  When loaded into the hardware simulator, the built-in Screen.hdl chip opens up a screen window; the simulator then refreshes this window from the screen memory map several times each second.
Simulated screen:

## Slide 36: Screen memory map
How to set the (row,col) pixel of the screen to black or to white:
Low-level (machine language): Set the col%16 bit of the word found at Screen[row*32+col/16] to 1 or to 0 (col/16 is integer division)
High-level: Use the OS command drawPixel(row,col)
(effects the same operation, discussed later in the course, when we’ll write the OS).
In the Hack platform, the screen is implemented as an 8K 16-bit RAM chip.
Notes: 36

## Slide 37: Keyboard
Keyboard chip: a single 16-bit register
Input: scan-code (16-bit value) of the currently pressed key, or 0 if no key is pressed
Output: same
How to read the keyboard:
Low-level (hardware): probe the contents of the Keyboard chip
High-level: use the OS command keyPressed()
(effects the same operation, discussed later in the course, when we’ll write the OS).
Special keys:
The keyboard is implemented as a built-in Keyboard.hdl chip. When this java chip is loaded into the simulator, it connects to the regular keyboard and pipes the scan-code of the currently pressed key to the keyboard memory map.
The simulated keyboard enabler button
Simulated keyboard:

## Slide 38: Memory: conceptual / programmer’s view
Using the memory:
To record or recall values (e.g. variables, objects, arrays), use the first 16K words of the memory
To write to the screen (or read the screen), use the next 8K words of the memory
To read which key is currently pressed, use the next word of the memory.
Data
Screen memory map
Keyboard map
Memory
Keyboard
Screen
Notes: 38

## Slide 39: Memory: physical implementation
Access logic:
Access to any address from 0 to 16,383 results in accessing the RAM16K chip-part
Access to any address from 16,384 to 24,575 results in accessing the Screen chip-part
Access to address 24,576 results in accessing the keyboard chip-part
Access to any other address is invalid.
load
out
in
16
15
16
RAM16K
(16K mem. chip)
address
0
16383
Screen
(8K mem. chip)
16384
24575
24576
Keyboard
(one register)
Memory
Keyboard
Screen
The Memory chip is essentially a package that integrates the three chip-parts RAM16K, Screen, and Keyboard into a single, contiguous address space.
This packaging effects the programmer’s view of the memory, as well as the necessary I/O side-effects.
Notes: 39

## Slide 40: CPU
CPU internal components (invisible in this chip diagram): ALU and 3 registers: A, D, PC
CPU execute logic:
The CPU executes the instruction according to the Hack language specification:
The D and A values, if they appear in the instruction, are read from (or written to) the respective CPU-resident registers
The M value, if there is one in the instruction’s RHS, is read from inM
If the instruction’s LHS includes M, then the ALU output is placed in outM, the value of the CPU-resident A register is placed in addressM, and writeM is asserted.
a Hack machine language instruction like M=D+M, stated as a 16-bit value

## Slide 41: CPU
CPU internal components (invisible in this chip diagram): ALU and 3 registers: A, D, PC
CPU fetch logic:
Recall that:
the instruction may include a jump directive (expressed as non-zero jump bits)
the ALU emits two control bits, indicating if the ALU output is zero or less than zero
If reset==0: the CPU uses this information (the jump bits and the ALU control bits) as follows:
If there should be a jump, the PC is set to the value of A; else, PC is set to PC+1
If reset==1: the PC is set to 0. (restarting the computer)
a Hack machine language instruction like M=D+M, stated as a 16-bit value
Notes: 41

## Slide 42: The C-instruction revisited

## Slide 43: CPU implementation
Execute logic:
Decode
Execute
Fetch logic:
If there should be a jump, set PC to A else set PC to PC+1
Cycle:
Execute
Fetch
Resetting the computer:
Set reset to 1, then set it to 0.
Chip diagram:
Includes most of the CPU’s execution logic
The CPU’s control logic is hinted: each circled “c” represents one or more control bits, taken from the instruction
The “decode” bar does not represent a chip, but rather indicates that the instruction bits are decoded somehow.

## Slide 44: Computer-on-a-chip interface

## Slide 45: Computer-on-a-chip implementation
CHIP Computer {
IN reset;
PARTS:
// implementation missing
}
Implementation: Simple, the chip-parts do all the hard work.

## Slide 46: Perspective: from here to a “real” computer
Caching
More I/O units
Special-purpose processors (I/O, graphics, communications, …)
Multi-core / parallelism
Efficiency
Energy consumption considerations
And more ...

## Slide 47
Turing Complete Devices can be rather simple
视频:
Coursera Video website: https://www.coursera.org/learn/build-a-computer
Building an 8-bit Computer :https://eater.net.

## Slide 48: See How a CPU Work
Notes: 48

## Slide 49: Computer Architecture: A Quantitative Approach
www.nand2tetris.org
Received Honorable
Professorship at
Tsinghua in 2018
He also set up the
RISC V research lab
@ Tsinghua
Shenzhen Campus
Notes: 49

## Slide 51: Formulas for Comp. Arch. I

## Slide 52: Formulas for Comp. Arch. II

## Slide 53: Formulas for Comp. Arch. III

## Slide 54: Formulas for Comp. Arch. IV

## Slide 55: Computing bottleneck is limited by Data Synchronization (Entanglement)

## Slide 56: How Internet Works by Ben Eater

## Slide 57: How to conduct counting and abstract counting reliably across spacetime?

## Slide 58: Main Thesis of today’s lecture: “How do you know that you know?” “Writing Technology” being the a way to help reach consensus?
https://raft.github.io/
https://lamport.azurewebsites.net/pubs/pubs.html

## Slide 59: Language Independent Analysis Methods
To ensure universality, one needs to be language/implementation agnostic
Mathematical Abstraction of Temporal Logic
http://www.kframework.org/
https://www.di.ens.fr/~cousot/AI/
Link to a short paper introducing TLA+

## Slide 60: A Cognitive Foundation X makes sense in Context Y
Huawei VP Mr. Yang Shaoqing
In a World Y where all things make sense
If you speak the language of X!

## Slide 61: Where is Paxos?

## Slide 62: Simplicity in NsM is Strategic!
The Named Roles in Paxos/Raft
  Proposers to present changes
  Learners to Authorize
  Learner to Execute
Governance Tools
  Holacracy
  Hypha-Decentralized Human Organization
Image Source: An Overview of Consensus Algorithms, by DxChain
Image Source: Hypha Project, by Hypha Earth

## Slide 63: Paxos Visualized

## Slide 64: A Talk on the subject of Paxos

## Slide 65: A Talk on the subject of Raft

## Slide 66: Kubernetes/ETCD and Raft
Notice that Kubernetes is the original form of Cybernetics.

## Slide 67: Namespace Management in Time

## Slide 68: The notion of Symmetry/Symmetry-breaking
Find a video or image showing the Trust-worthy Book Keeping comes from Symmetry and Symmetry-Breaking!

## Slide 69: How to move data in its simplest possible form?
Huawei VP Mr. Yang Shaoqing
Algorithms is about moving data!

## Slide 70: A Common Trick in Data Verification
Double Entry Ledger is a mechanism to leverage closure properties to verify data!
Double Entry Book Keeping was used as an example to explain the power of Symmetry/Invariance properties in Mathematics, not the only application
All fields of sciences and maths are grounded on invariance somehow.
https://plato.stanford.edu/entries/weyl/
“the root of all symmetry principles lies in the assumption that it is impossible to observe certain basic quantities” (p. 178 of Particle Physics and Introduction to Field Theory, New York: Harwood Academic Publishers.)

## Slide 71: Accountants and the Invention of Writing
Luca Pacioli published 26 pages of account balancing techniques in a math textbook
Accounting Balancing Equation
  Asset = Liability + Equity

## Slide 72: Double Entry Book Keeping is the foundation of Capitalism
复式记账是Pacioli最著名的科学贡献
Pacioli 是达芬奇的合作伙伴
Summa de arithmetica, geometria, proportioni et proportionalita （算术、几何、比例与可比性之总论）
  该书集成了代数、几何、逻辑、计算和记账的内容，包括复利计算等金融学的知识。
  是现代科学的奠基之作。
  “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric, … medieval merchants used double-entry bookkeeping as a rhetorical tool of capitalist propaganda, to persuade their ‘audience’ that their business was honest, morally sound and its profit-making ethically justified.”
  Excerpt From: Jane Gleeson-White. “Double Entry.”
1494年头版，1523年再版
Notes: “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric,”
Excerpt From: Jane Gleeson-White. “Double Entry.” Apple Books.

## Slide 73: Double Entry Bookkeeping and Linear Algebra
Notes: “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric,”
Excerpt From: Jane Gleeson-White. “Double Entry.” Apple Books.

## Slide 74: The Accounting Equation and Hamiltonian Mechanics
Accounting Balance Equation:
Assets = Liability + Equity
The structural similarity may seem to be simple in the beginning. But when put them in iterative procedures…
Notes: “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric,”
Excerpt From: Jane Gleeson-White. “Double Entry.” Apple Books.

## Slide 75: Hamiltonian Mechanics make energy Accountable
Assets = Liability + Equity
and
H = T + V
These two equations basically dominated two fields: Economics and Physical Sciences
Thinking from a Meta-Mathematical viewpoint,
they present a way to break down the total amount of conservative resources,
and therefore, allows iterative branching and therefore continuous replication.
Notes: “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric,”
Excerpt From: Jane Gleeson-White. “Double Entry.” Apple Books.

## Slide 76: Hamilton did more work on the Accounting Equation
The aim of this paper is to show how the mathematical basis is used for a precise treatment of double-entry bookkeeping, which was firstly developed in the nineteenth century by Sir William Rowan Hamilton. This is done by using basic notions of matrix algebra with the roots to the idea of using ordered pairs. We also reveal how the complex numbers and the rationals (fractions) developed in a mainstream of accounting science and became a leading platform for the ongoing processes within the Industry 4.0.
Image Source: Research Gate
Notes: In the presentation on Oct-9, 2020, Ray again, stated a link between the Atomic Explosion’s 20 thousands generations of chain reactions and the layers of Syntatic Trees in Chomsky’s Syntactic Theory about language. Then, he also reminded us that Chomsky and Shannon were working in locations that are 100 feet away from each other. The white and black dots are demonstrating the patterns of Fibonacci series.

## Slide 77: Kuhn Cycle: recursion and symmetry-breaking
Normal Science
Model
Drift
Model Crisis
Model Revolution
Paradigm
Change
Emerging cases or
systematic attacks
Ouroboros Snake
in five named stages
Keeping namespace consistent

## Slide 78: The second Language Design Strategy
combine structure with operations!
Put the Accounting /Hamiltonian equation in a matrix structure, the addition operations becomes iterative.
The isomorphism between accounting equation and the Hamiltonian formulation states: Science is about utilizing symmetries/invariance recursively.

## Slide 79: Concrete Activities in Daily Workflow
Image courtesy: Paladion Corporation Website Image source: https://www.paladion.net
What is DevSecOps?

## Slide 80: A short introduction video
https://youtu.be/j2m5YMnHvQQ

## Slide 81: Connecting Abstract and Concrete Domains
https://slideplayer.com/slide/8506871/
What is IMP?
Prof. Cousot and Koo in 2005

## Slide 82: The Basic Working Principle of Composition
https://slideplayer.com/slide/8506871/

## Slide 83: Arrow Chasing Computation
https://slideplayer.com/slide/8506871/

## Slide 84: Why is Simplicity in NsM so Strategic
Controlled Entropy = Controlled Time
  Think about Google’s interface
  Why are they removing buttons on iPhone?
  Bound Variables in Logics
When complexity is inevitable
  Leverage the notion of symmetry
  See Hermann Weyl’s quote on lacking information…
Image Source: Intro to System Science and Cybernetics,
Dr Paul Pangaro

## Slide 85
Moving Data in Traditional Workflows
https://youtu.be/p7-U1_E_j3w

## Slide 86
Data Sychronization with DevOps/CICD
https://youtu.be/p7-U1_E_j3w

## Slide 87: Instrumentation of DevOps
Image courtesy: PETSEBAN on NearCoding

## Slide 88: Personalized Digital Tools in Software Containers

## Slide 89
Asset Container | Operations | Tools
File(Document) | Content Editing | MediaWiki
File Directories | Changing File Structures | Git
Micro Services | Execute Programs | Docker
Configuration Data | Deployment & Maintenance | Kubernetes
Physical Environment | Physical Actions | Hackerspaces
Become aware of a new asset class

## Slide 90: Cloud Computing Reference Architecture

## Slide 91: TLA+ can help analyzed Architectural Properties

## Slide 92: Computing Architectures associated with Tools
Cloud Computing
Abstract Specification
Deterministic
Probabilistic
Centralized
Hybrid
Distributed
Single/Multi Core
Many Core
Single Site
Multi Site
Many Site
Hackerspaces
Super Computing Center
Notes: 92

## Slide 93: Summary
Think of computing devices as matrix processing machines
  Originated in the principle of symmetry (conservation laws)
    Presented in the format of double entry book keeping in 1491 book
Architectures can be defined by language specifications
  All vocabulary must be grounded in spacetime-energy metrics
  Syntax of languages can be formally analyzed through tools such as K-Framework
  Semantics of languages can be analyzed using Abstract Interpretation
Modern computing architecture is mostly hybrid
  Mobile and Cloud computing dominate usage and resources
  Computing results can be measured in Entropic terms
  The accounting practice of energy can be traced back to Hamilton and Pacioli

## Slide 94: Appendix