## Slide 1: Computational Thinking & Systems Design Lecture 12 Operating System: from bare minimum to distributed systems
Ben Koo
December 1, 2020

## Slide 2: Where we are at:
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12

## Slide 3: No Royal Road to Geometry. Euclid

## Slide 4: The Key Ideas in Shocken’s Lecture

## Slide 5: Jack revisited
/** Computes the average of a sequence of integers. */
class Main {
function void main() {
var Array a;
var int length;
var int i, sum;
let length = Keyboard.readInt(”How many numbers? ”);
let a = Array.new(length); // Constructs the array
let i = 0;
while (i < length) {
let a[i] = Keyboard.readInt(”Enter the next number: ”);
let sum = sum + a[i];
let i = i + 1;
}
do Output.printString(”The average is: ”);
do Output.printInt(sum / length);
do Output.println();
return;
}
}

## Slide 6: Jack revisited
/** Computes the average of a sequence of integers. */
class Main {
function void main() {
var Array a;
var int length;
var int i, sum;
let length = Keyboard.readInt(”How many numbers? ”);
let a = Array.new(length); // Constructs the array
let i = 0;
while (i < length) {
let a[i] = Keyboard.readInt(”Enter the next number: ”);
let sum = sum + a[i];
let i = i + 1;
}
do Output.printString(”The average is: ”);
do Output.printInt(sum / length);
do Output.println();
return;
}
}

## Slide 7: Typical OS functions
Language extensions / standard library
Mathematical operations (abs, sqrt, ...)
Abstract data types (String, Date, ...)
Output functions (printChar, printString ...)
Input functions (readChar, readLine ...)
Graphics functions (drawPixel, drawCircle, ...)
And more ...
System-oriented services
Memory management (objects, arrays, ...)
I/O device drivers
Mass storage
File system
Multi-tasking
UI management (shell / windows)
Security
Communications
And more ...

## Slide 8: The Jack OS
Math: Provides basic mathematical operations;
String: Implements the String type and string-related operations;
Array: Implements the Array type and array-related operations;
Output: Handles text output to the screen;
Screen: Handles graphic output to the screen;
Keyboard: Handles user input from the keyboard;
Memory: Handles memory operations;
Sys: Provides some execution-related services.

## Slide 9: Jack OS API
class Math {
function void init()
function int abs(int x)
function int multiply(int x, int y)
function int divide(int x, int y)
function int min(int x, int y)
function int max(int x, int y)
function int sqrt(int x)
}
Class String {
constructor String new(int maxLength)
method void dispose()
method int length()
method char charAt(int j)
method void setCharAt(int j, char c)
method String appendChar(char c)
method void eraseLastChar()
method int intValue()
method void setInt(int j)
function char backSpace()
function char doubleQuote()
function char newLine()
}
Class Array {
function Array new(int size)
method void dispose()
}
class Output {
function void moveCursor(int i, int j)
function void printChar(char c)
function void printString(String s)
function void printInt(int i)
function void println()
function void backSpace()
}
Class Screen {
function void clearScreen()
function void setColor(boolean b)
function void drawPixel(int x, int y)
function void drawLine(int x1, int y1, int x2, int y2)
function void drawRectangle(int x1, int y1, int x2, int y2)
function void drawCircle(int x, int y, int r)
}
class Memory {
function int peek(int address)
function void poke(int address, int value)
function Array alloc(int size)
function void deAlloc(Array o)
}
Class Keyboard {
function char keyPressed()
function char readChar()
function String readLine(String message)
function int readInt(String message)
}
Class Sys {
function void halt():
function void error(int errorCode)
function void wait(int duration)
}

## Slide 10: A typical OS:
Is modular and scalable
Empowers programmers (language extensions)
Empowers users (file system, GUI, ...)
Closes gaps between software and hardware
Runs in “protected mode”
Typically written in some high level language
Typically grows gradually, assuming more and more functions
Must be efficient.

## Slide 11: Success Criteria
Running Time Analysis (Performance/Efficiency)
Resource Allocation
Input Handling
Vector Graphics
Textual Outputs
Type Conversions
String Processing
.

## Slide 12: Abstraction
A well-defined set of Actions and iterative Branching Strategies
  A Roadmap of composable activities
  Sequencing and timing conditions
  Explicitly state dependencies and resource requirements
Why is abstraction useful?
  Allow reuse through universal properties
  Avoid resource conflicts
  Scale free and domain neutral
Concretization
Generalizing concrete experience?
  Make analogies in localized contexts
  Engage sensible metaphors
  Define terms and boundaries
Separate Specification from Abstraction

## Slide 13: Soundness
Every provable statement is true
Completeness
Every true statement is provable
Cited from : Soundness and Completeness: With Precision on news.ycombinator.com
https://youtu.be/3hspKYIn5ds?t=29
https://youtu.be/3hspKYIn5ds?t=162
For engineering/scientific purpose, it is difficult to escape Monism
The unifying notion of “Truth” is the source of Monism

## Slide 14: Efficiency
We have to implement various operations on n-bit binary numbers (n = 16, 32, 64, ...).
For example, consider multiplication
Naïve algorithm: to multiply x*y: { for i = 1 ... y do sum = sum + x }
Run-time is proportional to y
In a 64-bit system, y can be as large as 264.
Multiplications can take years to complete
Algorithms that operate on n-bit inputs can be either:
  Naïve: run-time is proportional to the value of the n-bit inputs
  Good: run-time is proportional to n, the input’s size.

## Slide 15: A historic moment remembered
… Wozniak began writing the software that would get the microprocessor to display images on the screen. After a couple of month he was ready to test it. “I typed a few keys on the keyboard and I was shocked! The letters were displayed on the screen.”
It was Sunday, June 29, 1975, a milestone for the personal computer. “It was the first time in history,” Wozniak later said, “anyone had typed a character on a keyboard and seen it show up on their own computer’s screen right in front of them”
(Steve Jobs, by Walter Isaacson, 2012)

## Slide 16: Keyboard input (cont.)

## Slide 17: Jack OS recap
class Math {
function void init()
function int abs(int x)
Class String {
Class Array {
function Array new(int size)
method void dispose()
}
class Output {
Class Screen {
class Memory {
function int peek(int address)
Class Keyboard {
Class Sys {
function void halt():
function void error(int errorCode)
function void wait(int duration)
}
Project 12:
Build it.
Implementation: just like GNU Unix and Linux were built:
Start with an existing system, and gradually replace it with a new system, one library at a time.

## Slide 18: Perspective
What we presented can be described as a:
  mini OS
  Standard library
Many classical OS functions are missing
No separation between user mode and OS mode
Some algorithms (e.g. multiplication and division) are standard
Other algorithms (e.g. line- and circle-drawing) can be accelerated with special hardware
And, by the way, we’ve just finished building the computer.

## Slide 19
Everything else was done by humans.
In CS, God gave us Nand
Here’s Nand; Go build a computer
Nand

## Slide 20: Example I: multiplication
Run-time: proportional to n
Can be implemented in SW or HW
Division: similar idea.

## Slide 21: Double Entry, Monks, Maths, and Magic

## Slide 22: Hamiltonian Mechanics make energy Accountable
Assets = Liability + Equity
and
H = T + V
These two equations basically dominated two fields: Economics and Physical Sciences
Thinking from a Meta-Mathematical viewpoint,
they present a way to break down the total amount of conservative resources,
and therefore, allows iterative branching and therefore continuous replication.
Notes: “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric,”
Excerpt From: Jane Gleeson-White. “Double Entry.” Apple Books.

## Slide 23: Hamilton did more work on the Accounting Equation
The aim of this paper is to show how the mathematical basis is used for a precise treatment of double-entry bookkeeping, which was firstly developed in the nineteenth century by Sir William Rowan Hamilton. This is done by using basic notions of matrix algebra with the roots to the idea of using ordered pairs. We also reveal how the complex numbers and the rationals (fractions) developed in a mainstream of accounting science and became a leading platform for the ongoing processes within the Industry 4.0.
Image Source: Research Gate
Notes: In the presentation on Oct-9, 2020, Ray again, stated a link between the Atomic Explosion’s 20 thousands generations of chain reactions and the layers of Syntatic Trees in Chomsky’s Syntactic Theory about language. Then, he also reminded us that Chomsky and Shannon were working in locations that are 100 feet away from each other. The white and black dots are demonstrating the patterns of Fibonacci series.

## Slide 24: Kan Extension and other ideas in Category Theory
Huawei VP Mr. Yang Shaoqing
https://youtu.be/9u1q3lH7VbE （video stops at 33:12）
All these terms are equivalent…
they can be refomulated into each other…

## Slide 25: Kan Extension makes concepts Representable
Huawei VP Mr. Yang Shaoqing

## Slide 26: The ideas of Universality
Huawei VP Mr. Yang Shaoqing
https://youtu.be/9u1q3lH7VbE?t=962（explaination starts at 16:02）

## Slide 27: When explaining the idea of Universal Properties …
Huawei VP Mr. Yang Shaoqing
We have explained certain aspects of all other properties in the ring.

## Slide 28: Example I: multiplication explained in Category Theory
Image Source: Wikipedia (through Wikiwand)

## Slide 29: Example II: square root
The square root function has two convenient properties:
  It’s inverse function is computed easily
  Monotonically increasing
Functions that have these two properties can be computed by binary search:
Number of loop iterations is bounded by n/2, thus the run-time is O(n).

## Slide 30: Math operations (in the Jack OS)
class Math {
function void init()
function int abs(int x)
function int multiply(int x, int y)
function int divide(int x, int y)
function int min(int x, int y)
function int max(int x, int y)
function int sqrt(int x)
}



class Math {
class String {
class Array {
class Output {
class Screen {
class Memory {
class Keyboard {
class Sys {
function (…)
…
}
The remaining functions are simple to implement.

## Slide 31: String processing (in the Jack OS)
Class String {
constructor String new(int maxLength)
method void dispose()
method int length()
method char charAt(int j)
method void setCharAt(int j, char c)
method String appendChar(char c)
method void eraseLastChar()
method int intValue()
method void setInt(int j)
function char backSpace()
function char doubleQuote()
function char newLine()
}
class Math {
class String {
class Array {
class Output {
class Screen {
class Memory {
class Keyboard {
class Sys {
function (…)
…
}

## Slide 32: Single digit ASCII conversions
asciiCode(digit) == digit + 48
digit(asciiCode) == asciiCode - 48

## Slide 33
SingleDigit–to-character conversions: done
Number–to-string conversions:
Converting a number to a string

## Slide 34: Memory management (in the Jack OS)
class Memory {
function int peek(int address)
function void poke(int address, int value)
function Array alloc(int size)
function void deAlloc(Array o)
}
class Math {
class String {
class Array {
class Output {
class Screen {
class Memory {
class Keyboard {
class Sys {
function (…)
…
}

## Slide 35: Memory management (naive)
The data structure that this algorithm manages is a single pointer: free.
When a program constructs (destructs) an object, the OS has to allocate (de-allocate) a RAM block on the heap:
  alloc(size): returns a reference to a free RAM block of size size
  deAlloc(object): recycles the RAM block that object refers to

## Slide 36
Memory management (improved)

## Slide 37: Peek and poke
class Memory {
function int peek(int address)
function void poke(int address, int value)
function Array alloc(int size)
function void deAlloc(Array o)
}
Implementation: based on our ability to exploit exotic casting in Jack:

## Slide 38: Graphics primitives (in the Jack OS)
Class Screen {
function void clearScreen()
function void setColor(boolean b)
function void drawPixel(int x, int y)
function void drawLine(int x1, int y1, int x2, int y2)
function void drawRectangle(int x1, int y1,int x2, int y2)
function void drawCircle(int x, int y, int r)
}
class Math {
class String {
class Array {
class Output {
class Screen {
class Memory {
class Keyboard {
class Sys {
function (…)
…
}

## Slide 39: A History of Graphics Acceleration Hardware
https://youtu.be/UUxUCVlXV0A

## Slide 40: Memory-mapped screen

## Slide 41: Pixel drawing
Implementation: using poke(address,value)

## Slide 42: Image representation: bitmap versus vector graphics
Bitmap file: 00100, 01010,01010,10001,11111,10001,00000, . . .
Vector graphics file: drawLine(2,0,0,5), drawLine(2,0,4,5), drawLine(1,4,3,4)
Pros and cons of each method.
(0,0)
vector
bitmap
pixel
Notes: 42

## Slide 43: Vector graphics: basic operations
drawPixel(x,y)
drawCircle(x,y,r)
drawLine(x1,y1,x2,y2)
drawRectangle(x1,y1,x2,y2)
1
2
3
4
5
6
7
8
9
0
1
2
3
4
5
6
7
8
9
10
11
12
13
0
drawLine(0,3,0,11)
drawRectangle(1,3,5,9)
drawLine(1,12,2,12)
drawLine(3,10,3,11)
drawLine(6,4,6,9)
drawLine(7,0,7,12)
drawLine(8,1,8,12)
(Primitive operation)
drawTriangle(x1,y1,x2,y2,x3,y3)
etc. (a few more similar operations)
1
2
3
.
.
.
0
1
2
3
.
.
.
0
Screen =
grid of pixels
Notes: 43

## Slide 44: How to draw a line?
drawLine(x1,y1,x2,y2)
Basic idea: drawLine is implemented through a sequence of drawPixel operations
Challenge 1: which pixels should be drawn ?
Challenge 2: how to draw the line fast ?
Simplifying assumption: the line that we are asked to draw goes north-east.
Notes: 44

## Slide 45: Line Drawing
Given: drawLine(x1,y1,x2,y2)
Notation: x=x1, y=y1, dx=x2-x1, dy=y2-y1
Using the new notation: We are asked to draw a line between (x,y) and (x+dx,y+dy)
set (a,b) = (0,0)
while there is more work to do
drawPixel(x+a,y+b)
decide if you want to go right, or up
if you decide to go right, set a=a+1; if you decide to go up, set b=b+1
set (a,b) = (0,0)
while (a ≤ dx) and (b ≤ dy)
drawPixel(x+a,y+b)
decide if you want to go right, or up
if you decide to go right, set a=a+1; if you decide to go up, set b=b+1
dx
dy
Notes: 45

## Slide 46: Line Drawing algorithm
drawLine(x,y,x+dx,y+dy)
set (a,b) = (0,0)
while (a ≤ dx) and (b ≤ dy)
drawPixel(x+a,y+b)
decide if you want to go right, or up
if you decide to go right, set a=a+1; if you decide to go up, set b=b+1
drawLine(x,y,x+dx,y+dy)
set (a,b) = (0,0)
while (a ≤ dx) and (b ≤ dy)
drawPixel(x+a,y+b)
if b/a > dy/dx set a=a+1 else set b=b+1
Oy Vey
Notes: 46

## Slide 47: Line Drawing algorithm, optimized
b/a > dy/dx is the same as a*dy < b*dx
Define diff = a*dy – b*dx
Let’s take a close look at this diff:
b/a > dy/dx is the same as diff < 0
When we set (a,b)=(0,0), diff = 0
When we set a=a+1, diff goes up by dy
When we set b=b+1, diff goes down by dx
drawLine(x,y,x+dx,y+dy)
set (a,b) = (0,0)
while (a ≤ dx) and (b ≤ dy)
drawPixel(x+a,y+b)
if b/a > dy/dx set a=a+1 else set b=b+1
drawLine(x,y,x+dx,y+dy)
set (a,b) = (0,0), diff = 0
while (a ≤ dx) and (b ≤ dy)
drawPixel(x+a,y+b)
if diff < 0 set a=a+1, diff = diff + dx else set b=b+1, diff = diff - dy
Motivation
When you draw polygons, e.g. in animation or video, you need to draw millions of lines
Therefore, drawLine must be ultra fast
Division is a very slow operation
Addition is ultra fast (hardware based)
Notes: 47

## Slide 48: Circle drawing
The screen origin (0,0) is at the top left.

## Slide 49: An anecdote about efficiency and design
… Jobs obsessed about the look of what would appear on the screen. One day Bill Atkinson burst into his office all excited. He had just come up with a brilliant algorithm that could draw circles onscreen quickly. The math for making circles usually required calculating square roots, which the Motorola 68000 microprocessor didn’t support. But Atkinson did a workaround based on the fact that the sum of a sequence of odd numbers produces a sequence of perfect squares (e.g. 1 + 3 = 4, 1 + 3 + 5 = 9, etc.)
When Atkinson fired up his demo, everyone was impressed except Jobs. “Well, circles are nice,” he said, “but how about drawing rectangles with rounded corners?”
(Steve Jobs, by Walter Isaacson, 2012)

## Slide 50: To sum up (vector graphics)…
To do vector graphics (e.g. display a PPT file), you have to draw polygons
To draw polygons, you need to draw lines
To draw lines, you need to divide
Division can be re-expressed as multiplication
Multiplication can be reduced to addition
Addition is easy.
Notes: 50

## Slide 51: Character output primitives (in the Jack OS)
class Output {
function void moveCursor(int i, int j)
function void printChar(char c)
function void printString(String s)
function void printInt(int i)
function void println()
function void backSpace()
}
class Math {
class String {
class Array {
class Output {
class Screen {
class Memory {
class Keyboard {
class Sys {
function (…)
…
}

## Slide 52: Character output
Given display: a physical screen, say 256 rows by 512 columns
We can allocate an 11 by 8 grid for each character
Hence, our output package should manage a 23 lines by 64 characters screen
Font: each displayable character must have an agreed-upon bitmap
In addition, we have to manage a “cursor”.

## Slide 53: Font implementation (in the Jack OS)
class Output {
static Array charMaps;
function void initMap() {
let charMaps = Array.new(127);
// Assign a bitmap for each character
do Output.create(32,0,0,0,0,0,0,0,0,0,0,0); // space
do Output.create(33,12,30,30,30,12,12,0,12,12,0,0); // !
do Output.create(34,54,54,20,0,0,0,0,0,0,0,0); // “
do Output.create(35,0,18,18,63,18,18,63,18,18,0,0); // #
...
do Output.create(48,12,30,51,51,51,51,51,30,12,0,0); // 0
do Output.create(49,12,14,15,12,12,12,12,12,63,0,0); // 1
do Output.create(50,30,51,48,24,12,6,3,51,63,0,0); // 2
. . .
do Output.create(65,0,0,0,0,0,0,0,0,0,0,0); // A ** TO BE FILLED **
do Output.create(66,31,51,51,51,31,51,51,51,31,0,0); // B
do Output.create(67,28,54,35,3,3,3,35,54,28,0,0); // C
. . .
return;
}
// Creates a character map array
function void create(int index, int a, int b, int c, int d, int e,
int f, int g, int h, int i, int j, int k) {
var Array map;
let map = Array.new(11);
let charMaps[index] = map;
let map[0] = a;
let map[1] = b;
let map[2] = c;
...
let map[10] = k;
return; }

## Slide 54: Keyboard primitives (in the Jack OS)
Class Keyboard {
function char keyPressed()
function char readChar()
function String readLine(String message)
function int readInt(String message)
}
class Math {
class String {
class Array {
class Output {
class Screen {
class Memory {
class Keyboard {
class Sys {
function (…)
…
}

## Slide 55: Keyboard input
If the RAM address of the keyboard’s memory map is known, the above logic can be implemented using a peek function
Problem I: the elapsed time between a “key press” and key release” events is unpredictable
Problem II: when pressing a key, the user should get some visible feedback (cursor, echo, ...).

## Slide 56: Some Final notes
CS is a science
What is science?
Reductionism
Life science: From Aristo (millions of rules) to Darwin (3 rules) to Watson and Crick (1 rule)
Computer science: We knew in advance that we could build a computer from almost nothing. In this course we actually did it.
Key lessons:
  Elegance
  Clarity
  Simplicity
  Playfulness.

## Slide 57: Operating System as a Program that Runs Forever -- Lamport

## Slide 58: Operating System as a Program that Runs Forever -- Lamport
https://youtu.be/6MJUGVFAXKg?t=114

## Slide 59: A Lattice-based Framework to analyze code

## Slide 60: Accountants’ Value Proposition
The International
Integrated Reporting
Framework
Dec. 2013
Notes: “historian James Aho linked double-entry bookkeeping to the ancient art of rhetoric,”
Excerpt From: Jane Gleeson-White. “Double Entry.” Apple Books.

## Slide 61: An Operating System based on Causal Structures of Events
https://youtu.be/hAWyex1GKRU?t=778

## Slide 62: Computational Laws and Consciousness
https://youtu.be/3WXTX0IUaOg?t=136

## Slide 63: It is all in the Names

## Slide 64: Saunders Mac Lane: Founder of Category Theory
Saunders Mac Lane (Wikipedia)
Categories, Functors and Natural Transformation.
Constructions on Categories.
Universals and Limits.
Adjoints.
Limits.
Monads and Algebras.
Monoids.
Abelian Categories.
Special Limits.
Kan Extensions.
Symmetry and Braiding in Monoidal Categories.
Structures in Categories.
Tables of Categories. Bibliography.

## Slide 65: From Monism, Dualism to Cyber-physical Systems
Image Source: Double-aspect Theory on Wikipedia

## Slide 66: Wiener’s Framing of Societal Values

## Slide 67: The Abstract and Concrete Domains
Kubernetes as the Control Plane
Dockerized app services as the
Data Plane

## Slide 68: Conclusion/Summary
A cognitive foundation based on Unitary Computing System:
  Easier to find isomorphism due to the compact Name Space
  Kan Extension refers to Adjoint Function/Galois Connection/Approximation
  Mathematical ideas named after human names shows that we are still belief in human
Cybernetics is being realized with tools such as Kubernetes:
  Many people can operate large scale named objects from distributed locations.
  A different model of governance/magic is lurking…